## Slide 1: Redundant Array of Inexpensive Disks (RAID)
Kartik Gopalan
Chapter 5 Tanenbaum’s book

## Slide 2: First Commercial Disk Drive

## Slide 3: RAID — Original Motivation
Replacing large and expensive mainframe hard drives (IBM 3310) by several cheaper Winchester disk drives
Will work but introduces a data reliability problem:
  Consider Mean Time To Failure (MTTF)
  Assume MTTF of a disk drive is 30,000 hours
  MTTF for a set of n drives is 30,000/n
    n = 10 means MTTF of 3,000 hours

## Slide 4: RAID — Today’s Motivation
“Cheap” hard drives are now big enough for most applications
We use RAID today for
  Increasing disk throughput by allowing parallel access
  Eliminating the need to make disk backups
    Disks are too big to be backed up efficiently

## Slide 5: Logical-to-Physical I/O Address Space Mapping
Logical I/O Space (block device)
Physical I/O Space
0
MAX
File Systems
READ / WRITE
SOFTWARE / FIRMWARE
BASED MAPPING

## Slide 6: Several Levels of RAID

## Slide 7: RAID 0
Striping
  Spread the data over multiple disk drives
No fault tolerance
But, much better I/O throughput
  Number of I/O operations per second
DISK 0 | DISK 1 | DISK 2 | DISK 3
BLOCK 0 | BLOCK 1 | BLOCK 2 | BLOCK 3
BLOCK 4 | BLOCK 5 | BLOCK 6 | BLOCK 7
BLOCK 8 | BLOCK 9 | BLOCK 10 | BLOCK 11
BLOCK 12 | BLOCK 13 | BLOCK 14 | BLOCK 15

## Slide 8: RAID 1
Mirroring
  Two copies of each disk block
Advantage
  Simple to implement
  Fault-tolerant
Disadvantage
  Requires twice the disk capacity
DISK 0 | DISK 1 | MIRROR 0 | MIRROR 1
BLOCK 0 | BLOCK 1 | BLOCK 0 | BLOCK 1
BLOCK 2 | BLOCK 3 | BLOCK 2 | BLOCK 3
BLOCK 4 | BLOCK 5 | BLOCK 4 | BLOCK 5
BLOCK 6 | BLOCK 7 | BLOCK 6 | BLOCK 7

## Slide 9: RAID 2
Use an error (detection + correction) code instead of duplicating the data blocks
Meant for disks that don’t have built-in error detection.
Modern disks support built-in error detection, so this level is mostly unused.
DISK 0 | DISK 1 | DISK 2 | PARITY 1 | PARITY 2
BLOCK 0 | BLOCK 1 | BLOCK 2 | F(0,1,2) | 
BLOCK 3 | BLOCK 4 | BLOCK 5 | F(3,4,5) | 
BLOCK 6 | BLOCK 7 | BLOCK 8 | F(6,7,8) | 
BLOCK 9 | BLOCK 10 | BLOCK 11 | F(9,10,11) | 
F = FUNCTION FOR ERROR DETECTION + CORRECTION

## Slide 10: XOR Primer
Truth Table
  0 XOR 0 = 0
  0 XOR 1 = 1
  1 XOR 0 = 1
  1 XOR 1 = 0
Associative and commutative
Lost any one bit? XOR the rest to recover.
  If 1 XOR (lost bit) = 0
  then lost bit = 1 XOR 0 = 1
Extends to any number of data bits
  If 1 XOR (lost bit) XOR 1 = 0
  then lost bit = 1 XOR 1 XOR 0 = 0

## Slide 11: RAID 3
N+1 disk drives: N data drives + 1 parity drive
Data Block b[k] partitioned into N fragments b[k,1], b[k,2], ... b[k,N]
Parity drive contains XOR (exclusive or) of these N fragments
    p[k] = b[k,1] XOR b[k,2] XOR ... XOR b[k,N]
Upon a failure, reconstruct the lost fragments by XOR of corresponding fragments from remaining drives.
  b[k,i] = p[k] XOR b[k,1] XOR ... b[k,i-1] XOR b[k,i+1] … XOR b[k,N]
Simple to implement in firmware/software
Permits only one I/O operation at a time over entire array
DISK 0 | DISK 1 | DISK 2 | PARITY
BLOCK [0,1] | BLOCK [0,2] | BLOCK [0,3] | PARITY 0
BLOCK [1,1] | BLOCK [1,2] | BLOCK [1,3] | PARITY 1
BLOCK [2,1] | BLOCK [2,2] | BLOCK [2,3] | PARITY 2
BLOCK [3,1] | BLOCK [3,2] | BLOCK [3,3] | PARITY 3

## Slide 12: RAID 4
Requires N+1 disk drives (as in RAID 3)
  N data drives + 1 Parity drive
Data striped at block granularity (as in RAID 0)
  Disk 1 has block 1, disk 2 has block 2, and so on.
Parity drive contains exclusive or of the N blocks in stripe
    p[k] = b[Nk] XOR b[Nk+1] XOR ... XOR b[Nk+N-1]
Multiple Read I/O operations can be processed in parallel
But how about parallel writes I/O operations?
DISK 0 | DISK 1 | DISK 2 | PARITY
BLOCK 0 | BLOCK 1 | BLOCK 2 | PARITY 0
BLOCK 3 | BLOCK 4 | BLOCK 5 | PARITY 1
BLOCK 6 | BLOCK 7 | BLOCK 8 | PARITY 2
BLOCK 9 | BLOCK 10 | BLOCK 11 | PARITY 3

## Slide 13: RAID 5
Single parity drive of RAID-4 is involved in every write
  Will limit write parallelism
  Exercises one parity disk more than others
Solution in RAID-5
  Distribute the parity blocks among all N+1 drives
Up to N/2 parallel writes
DISK 0 | DISK 1 | DISK 2 | DISK 3
BLOCK 0 | BLOCK 1 | BLOCK 2 | PARITY 0
BLOCK 3 | BLOCK 4 | PARITY 1 | BLOCK 5
BLOCK 6 | PARITY 2 | BLOCK 7 | BLOCK 8
PARITY 3 | BLOCK 9 | BLOCK 10 | BLOCK 11

## Slide 14: The write problem
What happens when we want to update a single block?
  Block belongs to a stripe
  Every time a block is updated, the parity must be updated as well.
Problem: How do we compute the new parity?
...
b[Nk+1]
p[k]
b[Nk+2]
b[Nk]

## Slide 15: First (naïve) solution
Read values of N-1 other blocks in stripe
Re-compute
  p[k] = b[Nk] XOR b[Nk+1] XOR ... XOR b[Nk+N-1]
Solution requires
  N-1 reads
  2 writes (new block and parity block)

## Slide 16: Second solution
Assume we want to update block b[Nk+i]
Read old values of b[Nk+i] and parity block p[k]
Compute
  p[k] = new b[Nk+i] XOR old b[Nk+i] XOR old p[k]
Solution requires
  2 reads (old values of block and parity block)
    Or just one read, if old b[Nk+i] kept in memory.
  2 writes (new block and parity block)

## Slide 17: Comparison
 | RAID 0 (N disks) | RAID 1 (N disks) | RAID 2 (N+1) disks | RAID 3 (N+1) disks | RAID 4 (N+1) disks | RAID 5 (N+1) disks
Fault-tolerance | None | All 1-disk and most 2-disk failures | 1-disk failure with error detection and correction | 1-disk failure with Error Correction | 1-disk failure with Error Correction | 1-disk failure with Error Correction
Max. READ Parallelism | N | N | N | 1 (none) | N | N+1
Max. WRITE Parallelism | N | N/2 | 1 (none) | 1 (none) | 1 (none) | (N+1)/2
Space Overhead | 0% | 100% | (k/N)x100% for K parity disks | (1/N)x100% | (1/N)x100% | (1/N)x100%

## Slide 18: Conclusion
RAID original purpose was to take advantage of commodity drives that were smaller and cheaper than conventional disk drives
  Replace a single large drive by an array of smaller drives
Nobody does that anymore!
Today: Main purpose of RAID is to build fault-tolerant storage systems that do not need backups and deliver high throughput.
Low cost of disk drives makes RAID-1 attractive for small installations
  We have now very cheap RAID controllers
Otherwise prefer
  RAID-3 for simplicity
  RAID-5 for higher parallelism
Often combined with NVRAM to improve write performance